## Slide 1
Green Corridor
Ammonia Bunkering Optimization
MILP Model Analysis & Results

## Slide 2
Executive Summary
Metric | Value
Operational Scenarios | 3 cases
Feasible Solutions | 270 total
Case 1 Optimal NPC | $153.5M
Best Case (Ulsan) | $94.9M (-38%)
Optimal Shuttle Size | 2,500-5,000 m³

## Slide 3
Case 1: Busan Port Storage
Storage-based bunkering at Busan Port (intra-port transfer)
Optimal Configuration:
• Shuttle Size: 2,500 m³
• Pump Capacity: 2,000 m³/h
• NPC (20 years): $153.5M
Characteristics:
• Large storage tank (35,000 tons)
• 2.0 hour intra-port travel time
• Higher storage cost burden

## Slide 4
Case 2-1: Yeosu Route
Long-distance shuttle route: Yeosu → Busan (86 nm)
Optimal Configuration:
• Shuttle Size: 5,000 m³
• Pump Capacity: 2,000 m³/h
• NPC (20 years): $158.2M
Performance vs Case 1:
• +3.1% more expensive
• Travel Time: 5.73 hours
• No storage cost (26% savings)
• Higher fuel consumption

## Slide 5
Case 2-2: Ulsan Route
OPTIMAL
Short-distance shuttle route: Ulsan → Busan (25 nm)
Optimal Configuration:
• Shuttle Size: 5,000 m³
• Pump Capacity: 2,000 m³/h
• NPC (20 years): $94.9M
Performance vs Case 1:
✓ -38.2% cost reduction (BEST OPTION)
• Travel Time: 1.67 hours (shortest)
• 33% lower fuel consumption vs Yeosu
• Lowest total NPC

## Slide 6
NPC Heatmaps: Shuttle Size vs Pump Flow Rate

## Slide 7
Top 10 Cost Breakdown by Component

## Slide 8
Case Comparison: NPC, Equipment, Cost

## Slide 9
NPC Distribution Analysis

## Slide 10
Sensitivity Analysis: Shuttle Size Impact

## Slide 11
Key Findings
Ulsan Route Optimal
38.2% cost reduction vs Busan ($94.9M vs $153.5M)
Storage Tank Burden
Tank CAPEX ($28.9M) limits Case 1 competitiveness
Equipment Sizing
5,000 m³ shuttles optimal for long-distance routes
Distance Critical
25 nm route reduces fuel by 33% vs 86 nm route

## Slide 12
NPC Breakdown by Component (20-Year Horizon)
Cost Component | Case 1 | Case 2-1 | Case 2-2
Total NPC | $153.5M | $158.2M | $94.9M
Shuttle CAPEX | $24.8M | $24.1M | $24.1M
Bunkering CAPEX | $9.8M | $9.8M | $9.8M
Tank CAPEX | $28.9M | $0 | $0
Total OPEX | $90.0M | $124.3M | $61.0M

## Slide 13
Economic Analysis & Equipment Requirements
Case 1 Initial Shuttles
6
Case 2-1 Initial Shuttles
8
Case 2-2 Initial Shuttles
8
Cost per Tonne (Case 1)
~$45
Cost per Tonne (Case 2-2)
~$28
Ulsan route fuel consumption 33% lower due to shorter distance (25 nm vs 86 nm)

## Slide 14
Strategic Recommendations
1. Prioritize Ulsan Route: Deploy infrastructure toward Case 2-2 for 38% cost savings
2. Optimize Fleet: Use 5,000 m³ shuttles for long-distance, 2,500 m³ for storage-based
3. Reassess Storage: High tank CAPEX ($28.9M) limits Case 1 competitiveness
4. Phased Deployment: Start with 6-8 shuttles in 2030, grow 10% annually

## Slide 15
Implementation Roadmap
2030
Foundation: 6-8 shuttles, 35 vessels
2035
Growth: 10-12 shuttles, 100+ vessels
2040
Scaling: Optimize efficiency, 200+ vessels
2050
Maturity: 500 vessels, integrated supply chain

## Slide 16
Methodology Overview
Optimization Model:
MILP (Mixed-Integer Linear Programming)
Objective:
Minimize total Net Present Cost across 2030-2050
Decision Variables:
Fleet size, shuttle/pump specifications, bunkering cycles
Cost Components:
CAPEX (vessels, equipment, storage), OPEX (fuel, maintenance, cooling)
Discount Rate:
7% annual for NPV calculations
Solver:
CBC (Coin-or Branch and Cut) via PuLP with <0.1% optimality gap

## Slide 17
Conclusion
Ulsan Route (Case 2-2) is the Economically Optimal Solution
Achieves $94.9M NPC over 20 years—38.2% cost reduction vs Busan storage scenario
Strategic Implications
Development should focus on Ulsan infrastructure with 5,000 m³ shuttles and 2,000 m³/h pumps
to serve Green Corridor vessels economically through 2050
Next Steps
Proceed with detailed feasibility analysis for Ulsan infrastructure, port coordination, and phased fleet deployment

## Slide 18
Questions?
Green Corridor Ammonia Bunkering Optimization
Infrastructure Planning 2030-2050